## Slide 1
B.SC. THESIS DEFENSE · DEPARTMENT OF CSE · NPI UNIVERSITY OF BANGLADESH
UniBus Live
A Real-Time Bilingual University Bus Tracking System
with Reliable Dual-Source GPS Acquisition
Md. Shishir Hossain
ID 0852220005101005 · Batch 12th
Md. Sajib Hasan
ID 0852220005101008 · Batch 12th
Md. Showkat Hossen
ID 0852220005101009 · Batch 12th
Supervisor: Mahbubur Rahman Chowdhury, Senior Lecturer, Dept. of CSE, NPIUB
18 July 2026

## Slide 2
THE PROBLEM
Waiting for a bus you cannot see
A student at the stop has no way to know: did the bus leave 5 minutes ago — or is it 15 minutes away?
⏱
Missed buses
The bus passed early; the student finds out too late.
🌧
Long, uncertain waits
Standing in heat or rain for time that could be saved.
💸
No usable product
Commercial trackers: costly, operator-facing, English-only.
Our goal: let every student see their bus live, with the arrival time at their own stop — in their own language.
UniBus Live · Thesis Defense
2

## Slide 3
OUR SOLUTION
UniBus Live — one platform, four parts
PRIMARY SOURCE
GPS Tracker
Concox GT06S fixed in the bus.
Fully automatic — no driver needed.
FOR STUDENTS
Passenger App
Live map · per-stop arrival times ·
alerts · English + বাংলা
BACKUP SOURCE
Driver App
Opt-in backup publisher —
used only when needed.
FOR TRANSPORT OFFICE
Admin Console
Routes · schedules · fleet ·
live operations map.
Everything runs on one low-cost server — Node.js · PostgreSQL · Redis · Traccar · Socket.IO. No paid cloud services.
UniBus Live · Thesis Defense
3

## Slide 4
THE PASSENGER EXPERIENCE
The map is never blank
Before departure
Bus visible at the depot — "getting ready", not a blank map.
On route, live
Next stop and minutes away, updated in seconds.
Today's schedules
Every route and departure at a glance.
English + বাংলা
The whole app in the rider's language.
Get-off alert: a push notification when the bus is within 80 m of your stop — even if the app is closed.
UniBus Live · Thesis Defense
4

## Slide 5
SYSTEM ARCHITECTURE
Three layers, one low-cost server
Vehicle layer
Tracker reports every 5 s over GSM; driver phone is only a fallback.
One backend server
Traccar decodes · Node.js validates, computes ETAs, broadcasts · PostgreSQL + Redis.
Client layer
Passenger app and admin console — pushed over WebSocket, not polled.
UniBus Live · Thesis Defense
5

## Slide 6
REAL-TIME DATA FLOW
From GPS fix to the student's screen
5.9 s median
from GPS fix on the bus to the server — measured over 46,286 real fixes.
1–2
Capture & decode — every 5 s, decoded in ≈1 s
3–4
Pick best source · reject faulty readings
5
Compute the ETA for every stop ahead
6–7
Store, publish, push to every subscribed phone
UniBus Live · Thesis Defense
6

## Slide 7
RELIABLE BY DESIGN
Two independent sources, one automatic choice
PRIMARY — GPS TRACKER
Works completely on its own
• Hard-wired in the bus, reports every 5 s
• Trip starts automatically from its data
• No driver action, phone, or data plan needed
BACKUP — DRIVER'S PHONE (OPT-IN)
Only when a trip needs it
• Driver must be assigned and start sharing
• Covers buses without a tracker yet
• Normal operation never depends on it
The server scores both sources on every fix and picks the best one automatically
tracker preferred when healthy · switches mid-trip with no visible jump · what is automatic is the selection
UniBus Live · Thesis Defense
7

## Slide 8
SMART ARRIVAL TIMES
A simple estimator that works from day one
ETA = remaining distance along the route ÷ recent average speed
computed for every stop ahead, on every accepted GPS fix
Route-aware
The fix is projected onto the route line, so sideways GPS error doesn't break the estimate.
Honest confidence
Every estimate is labeled High / Medium / Low from the quality of the speed signal.
No training data
Works from the first day — while logging every prediction so an ML model can come later.
Arrival radius 80 m — reaching it marks the stop and fires the rider's get-off alert.
UniBus Live · Thesis Defense
8

## Slide 9
THE PILOT
Seven weeks on the real fleet — zero simulation
7
weeks live
6 May – 23 Jun 2026
9
routes
3
buses (1 with
hardware tracker)
38
registered riders
71
completed trips
46,548
GPS reports ingested
Every number in this defense comes from the production database of this pilot.
UniBus Live · Thesis Defense
9

## Slide 10
RESULT · SPEED
The map reflects reality within seconds
5.9 s
median latency, GPS fix → server
Bounded mainly by the 8 s polling interval — push delivery itself takes ≈1 s. A further 1.2 s (median) to persist each fix.
Latency across 46,286 fixes (seconds)
Median
5.9 s
Mean
7.4 s
90th percentile
9.9 s
95th percentile
11.1 s
UniBus Live · Thesis Defense
10

## Slide 11
RESULT · RELIABILITY & ENGAGEMENT
The backup carried real weight
Which source tracked the 70 sourced trips?
64% GPS tracker (45 trips)
36% phone backup (25)
The 36% were mostly the two buses not yet fitted with trackers — coverage never stopped. Fleet-wide trackers will shrink this to a rare safety net.
80%
of arrival & service notifications were read by riders (36 of 45)
80 m
arrival radius that triggers the get-off alert
0
passenger-visible jumps during mid-trip source handovers
UniBus Live · Thesis Defense
11

## Slide 12
A HIDDEN PROBLEM — FOUND & FIXED
The pilot's most valuable discovery
98%
of 46,548 GPS reports were pure waste
buses kept transmitting every 5 seconds even while parked overnight — only 864 reports fell inside a real trip
→
60×
less parked-time reporting after our fix
device: 5 s → 300 s when parked (one SMS: TIMER,5,300#) · server polling: 8 s → 60 s when idle
Invisible in design, unmistakable in real data — and fixed at both the device and the server without touching live tracking.
UniBus Live · Thesis Defense
12

## Slide 13
THE ADMIN CONSOLE
The transport office sees everything
Live operations — whole fleet at a glance
Route builder — stops, distance, travel time on the map
Also: buses, GPS devices, schedules, stops, users, analytics — one web console, same API as the apps.
UniBus Live · Thesis Defense
13

## Slide 14
THE DRIVER APP
The opt-in backup, kept deliberately simple
Shares nothing by default
Location goes out only between Start trip and End trip.
Choose the source
Bus device or my phone — visible on screen.
Live self-check
Driver sees speed, GPS accuracy and update age while publishing.
Drivers only
Assigned driver + driver role required — an authorization boundary.
UniBus Live · Thesis Defense
14

## Slide 15
HONEST LIMITS & WHAT'S NEXT
A feasibility pilot, and a roadmap
LIMITATIONS
• Small pilot: 7 weeks, 3 buses, 38 riders
• Only one bus carried the hardware tracker
• ETA error (MAE) still accumulating — every prediction is logged for it
• Timetable linkage incomplete during the pilot
FUTURE WORK
• ML arrival prediction trained on our logged trip history
• Trackers on every bus — phone becomes a rare safety net
• Ignition-wired (ACC) reporting: device sleeps with the engine
• Occupancy info and a formal usability study at larger scale
UniBus Live · Thesis Defense
15

## Slide 16
Thank you
Questions welcome — every number is from our production database.
5.9 s
median latency
46,548
GPS reports
71
real trips
64 / 36
tracker vs phone
60×
idle waste cut
80%
alerts read
UniBus Live · Team UniBus · Dept. of CSE · NPI University of Bangladesh